Date

(mail address)

Re: Plan Review – (address)

Dear (name),

Upon a review of the construction documents submitted for the above referenced property.  The following code issues are being brought to your attention now because they may not have been clearly indicated on the construction documents.  Compliance with these items will avoid any unnecessary delays during construction and are required prior to the final certificate of occupancy being issued

The swimming pool must comply with the 2018 International Swimming Pool and Spa Code.

All wiring for the swimming pool must comply with the 2018 International Swimming Pool and Spa Code:

# 302.1 Electrical.

Electrical requirements for aquatic facilities shall be in accordance with NFPA 70 or the International Residential Code, as applicable in accordance with Section 102.7.1.

Exception: Internal wiring for portable residential spas and portable residential exercise spas.

# 305.2 Outdoor swimming pools and spas.

Outdoor pools and spas and indoor swimming pools shall be surrounded by a barrier that complies with Sections 305.2.1 through 305.7.

# 305.2.1 Barrier height and clearances.

Barrier heights and clearances shall be in accordance with all of the following:

- The top of the barrier shall be not less than 48 inches (1219 mm) above grade where measured on the side of the barrier that faces away from the pool or spa. Such height shall exist around the entire perimeter of the barrier and for a distance of 3 feet (914 mm) measured horizontally from the outside of the required barrier.

- The vertical clearance between grade and the bottom of the barrier shall not exceed 2 inches (51 mm) for grade surfaces that are not solid, such as grass or gravel, where measured on the side of the barrier that faces away from the pool or spa.

- The vertical clearance between a surface below the barrier to a solid surface, such as concrete, and the bottom of the required barrier shall not exceed 4 inches (102 mm) where measured on the side of the required barrier that faces away from the pool or spa.

- Where the top of the pool or spa structure is above grade, the barrier shall be installed on grade or shall be mounted on top of the pool or spa structure. Where the barrier is mounted on the top of the pool or spa, the vertical clearance between the top of the pool or spa and the bottom of the barrier shall not exceed 4 inches (102 mm).

# 305.2.2 Openings.

Openings in the barrier shall not allow passage of a 4-inch-diameter (102 mm) sphere.

# 305.3 Gates.

Access gates shall comply with the requirements of Sections 305.3.1 through 305.3.3 and shall be equipped to accommodate a locking device. Pedestrian access gates shall open outward away from the pool or spa, shall be self-closing and shall have a self-latching device.

# 305.3.1 Utility or service gates.

Gates not intended for pedestrian use, such as utility or service gates, shall remain locked when not in use.

# 305.3.2 Double or multiple gates.

Double gates or multiple gates shall have not fewer than one leaf secured in place and the adjacent leaf shall be secured with a selflatching device. The gate and barrier shall not have openings larger than 1/2 inch (12.7 mm) within 18 inches (457 mm) of the latch release mechanism. The self-latching device shall comply with the requirements of Section 305.3.3.

# 305.3.3 Latches.

Where the release mechanism of the self-latching device is located less than 54 inches (1372 mm) from grade, the release mechanism shall be located on the pool or spa side of the gate not less than 3 inches (76 mm) below the top of the gate, and the gate and barrier shall not have openings greater than 1/2 inch (12.7 mm) within 18 inches (457 mm) of the release mechanism.

# 305.4 Structure wall as a barrier.

Where a wall of a dwelling or structure serves as part of the barrier and where doors or windows provide direct access to the pool or spa through that wall, one of the following shall be required:

- Operable windows having a sill height of less than 48 inches (1219 mm) above the indoor finished floor and doors shall have an alarm that produces an audible warning when the window, door or their screens are opened. The alarm shall be listed and labeled as a water hazard entrance alarm in accordance with UL 2017.

The above items are not all-inclusive and the written text of the 2018 IRC as amended by Act 45/1999 shall apply.  Please do not hesitate to call should you have any questions.

Sincerely,

CODE.SYS CODE CONSULTING, INC.

Inspector

Cc:  file